## Slide 1
44 bunches
44 bunches
44 bunches
6 ns spacing
100 ns gap
1 RF pulse, 1 microsecond long
20 RF pulse at 300 Hz, 63 millisecond long
Repeat at 5 Hz
ILC Positron Train (2015): https://academic.oup.com/ptep/article/2015/10/103G01/2461005

## Slide 2: ILC 2020
The ILC operates at 5 Hz and one pulse contains 1312 bunches. Prior to acceleration by the main Linac, all bunches should be ready in the DR. Therefore, 1312 bunches are prepared in the pulse interval of 200 ms. Since the DR is designed to damp the bunches within 100 ms to achieve low emittance, we can use 100 ms for positron production. In the proposed electron-driven positron source, positrons for one pulse (1312 bunches) are generated as 20 sub-pulses at a repetition rate of 300 Hz. The first 12 sub-pulses consist of two 33 bunch mini-trains whereas the last 8 pulses consist of 33 and 32 bunch mini-trains, so that 1312 bunches are generated in 64 ms. In Fig. 2, we show the bunch structure of a sub-pulse containing two 33 bunches. The heat load on the target is significantly relaxed using this pulse structure compared to the undulator scheme, because the heat associated with only 66 (or 65) bunches is accumulated. In comparison, 1312 bunches are created in 1 ms for the undulator scheme. The generated positrons are stored in the DR for 136 ms, which is enough for radiation damping, and sent to the main linac (ML) and the interaction point (IP) [2].

## Slide 3
33 bunches
33 bunches
6 ns spacing
80 ns gap
1 RF pulse, 474 ns long
20 RF pulse at 300 Hz, 64 millisecond long
Repeat at 5 Hz
ILC Positron Train (2020): https://www.sciencedirect.com/science/article/pii/S016890021931455X
3.3 ms gap
Energy deposition calculation:
Initial beam energy = 3 GeV
Energy deposition frac = 0.18
Bunch charge (e-/bunch) = 2.5E10
Energy dep/bunch = 2.16 J
Energy dep/mini train (66) = 143 J
Energy dep/full train (1312) = 2.86 kJ
Energy dep/s = 14.3 kJ/s
Energy of vaporization:
Radius = 6 mm
Length = 12.9 cm
Volume = 14.6 cm^3
Heat of vap/vol = 284.2 J/cm^3
Energy to vaporize = 4.15 kJ
Flow rate:
Volume = 14.6 cm^3
Train spacing = 200 ms
Flow rate = 0.073 L/s
Energy deposition calculation:
Initial beam energy = 3 GeV
Energy deposition frac = 0.23
Bunch charge (e-/bunch) = 2.5E10
Energy dep/bunch = 2.76 J
Energy dep/full train (1312) = 3.62 kJ
Energy dep/s = 18.1 kJ/s
PEDD (per full train) = 84 J/g
Bunches to vaporize = 1,503

## Slide 4
5.26 ns spacing
1 RF pulse, 700 ns long
Repeat at 120 Hz
C^3 Positron Train: https://arxiv.org/pdf/2110.15800.pdf
Energy deposition calculation:
Initial beam energy = 3 GeV
Energy deposition frac = 0.23
Bunch charge = 7.8E9
Energy dep/bunch = 0.862 J
Energy dep/full train (133) = 114.6 J
Energy dep/s = 13.76 kJ/s
PEDD (train) = 2.66 J/g
Energy of vaporization:
Radius = 6 mm
Length = 12.9 cm
Volume = 14.6 cm^3
Heat of vap/vol = 284.2 J/cm^3
Energy to vaporize = 4.15 kJ
Flow rate:
Volume = 14.6 cm^3
Train spacing = 8.33 ms
Flow rate = 1.75 L/s
Volume = 14.6 cm^3
Total time to vaporize (36 trains) = 300 ms
Flow rate = 0.0487 L/s
133 bunches
5.26 ns spacing
1 RF pulse, 700 ns long
133 bunches
8.33 ms gap

## Slide 5
“Optimal”: Optimal is defined as minimizing flow rate
What are our assumptions?
Roughly 1e14 e+/s delivered to IP
Safety factor of 1.5 after target
Yield of 1.2
This means 1.25e14 e-/s on target
Assume 3 GeV and 0.18 fraction deposited
  8.65e-11 J/e-
10.81 kJ/s deposited in target
4.15 kJ to vaporize one LXe volume
2.6 LXe volumes/s = 0.038 L/s
Therefore:
Run bunch trains at 2.5 Hz
Each bunch train has 4e13 electrons
Then each train evaporates one volume of LXe
Assume 10 GeV and 0.23 fraction deposited
  3.685e-10 J/e-
46.06 kJ/s deposited in target
4.15 kJ to vaporize one LXe volume
Flow Rate (8.7 LXe volumes/s) = 0.162 L/s
Time to vaporize = 90.1 ms
Therefore:
Run bunch trains at 11.10 Hz
Each bunch train has 1.125e13 electrons
Then 1000 bunches per train if each bunch is 1.125e10 electrons
Then each train evaporates one volume of LXe
PEDD = 96.1 J/g

## Slide 6
1 RF pulse
Repeat at 2.5 Hz
“Optimal”: Optimal is defined as minimizing flow rate
Energy deposition calculation:
Initial beam energy = 3 GeV
Energy deposition frac = 0.18
Bunch charge = 4E10
Energy dep/bunch = 0.865 J
Energy dep/full train (1000) = 3.46 kJ
Energy dep/s = 8.65 kJ/s
Energy of vaporization:
Radius = 6 mm
Length = 12.9 cm
Volume = 14.6 cm^3
Heat of vap/vol = 284.2 J/cm^3
Energy to vaporize = 4.15 kJ
Flow rate:
Volume = 14.6 cm^3
Total time to vaporize (1 train) = 400 ms
Flow rate = 0.0365 L/s
1000 bunches
1000 bunches
400 ms gap

## Slide 7
 | FACET-II | ILC | C3 | Optimal
Energy (GeV) | 10 | 3 | 3 | 3
Charge (#elec e10) | 1.25 | 2.5 | 0.78 | 4
Bunches/train | 1 | 1312 | 133 | 1200
Rep rate (Hz) | 10 | 5 | 120 | 2.6
PEDD (train) J/g | 0.02 | 66.5 | 2.1 | 96.5
Flow rate (train) L/s | 1.3e-5 | 0.073 | 1.75 | 0.038